## Slide 1: INTRODUCTION TO CONTROL SYSTEM CODE: COB 3134 UQF 7 - B
Prepared by: Vicent V.M., MSc.
Nov., 2021

## Slide 2: Learning Context
Control system definitions; principles of feedback control system; control system block diagrams model; control flow diagram model; mathematical modelling of control system; sensitivity, transient response; stability criteria; steady state error; root locus methods; transfer functions
So as to have the:
    Ability to define the control system
    Ability to draw signal flow block diagram
    Ability to describe a control system
    Explain basic principles of control system
    Calculate stability parameters
    Derive mathematical model of the control system
    Ability to derive a transfer function of the control system

## Slide 3: Introduction to Control System Engineering
Engineering is concerned with understanding and controlling the materials and forces of nature for the benefit of humankind.
Control system engineers are concerned with understanding and controlling segments of their environment, often called systems, to provide useful economic products for society. The twin goals of understanding and controlling are complementary because effective systems control requires that the systems be understood and modelled.
Therefore:
A control system is an interconnection of components forming a system configuration that will provide a desired system response

## Slide 4: Open – loop control System (without feedback)
The basis for analysis of a system is the foundation provided by linear system theory, which assumes a cause–effect relationship for the components of a system.
Therefore a component or process to be controlled can be represented by a block, as shown in figure 1.1. The input–output relationship represents the cause-and-effect relationship of the process, which in turn represents a processing of the input signal to provide an output signal variable, often with a power amplification. An open-loop control system utilizes a controller or control actuator to obtain the desired response, as shown in figure 1.2. An open-loop system is a system without feedback.
Process -

## Slide 5: Cont..
Fig. 1.1: Process to be controlled
Fig. 1.2: Open - loop control system
Therefore:
An open – loop control system utilizes an actuating device to control the process directly without using feedback

## Slide 6: Cont..
Advantages of Open-Loop Control System
The followings are the advantages of an open-loop control system:
These systems are simple in construction and design.
These systems are economical.
These systems are easy from maintenance point of view.
Usually these systems are not much troubled with problems of stability.
These systems are convenient to use when output is difficult to measure

## Slide 7: Cont..
Disadvantages of Open-Loop Control System
The followings are the disadvantages of an open-loop control system:
These systems are not accurate and reliable because their accuracy dependent on the accuracy of calibration.
In these systems, inaccuracy results are obtained with parameter variations i . e . internal disturbances.
Recalibration of the controller is required from time to time for maintaining quality and accuracy
Any change in output cannot be corrected automatically

## Slide 8: Closed-Loop Control System (with feedback)
In contrast to an open-loop control system, a closed-loop control system utilizes an additional measure of the actual output to compare the actual output with the desired output response. The measure of the output is called the feedback signal. A simple closed-loop feedback control system is shown in figure 1.3. A feedback con- trol system is a control system that tends to maintain a prescribed relationship of one system variable to another by comparing functions of these variables and using the difference as a means of control.
  A feedback control system often uses a function of a prescribed relationship between the output and reference input to control the process.

## Slide 9: Cont..
Fig. 1.3: Closed –loop feedback control system
Therefore:
A closed – loop control system uses a measurement of the output and feedback of this signal to compare it with the desired output (reference or command)

## Slide 10: Cont..
Due to the increasing complexity of the system under control and the interest in achieving optimum performance, the importance of control system engineering has grown in the past decade. Furthermore, as the systems become more complex, the interrelationship of many controlled variables must be considered in the control scheme. A block diagram depicting a multivariable control system is shown in figure below

## Slide 11: Cont..
Example of closed loop control system
Consider electric clothes dryer:
Suppose we used a sensor or transducer (input device) to continually monitor the temperature or dryness of the clothes and feed a signal relating to the dryness back to the controller as shown below

## Slide 12: Cont..
This sensor monitors the actual dryness of the clothes and compare it with (or subtract it from) the input reference. The error signal (error = required dryness – actual dryness) is amplified by the controller, and the controller output makes the necessary correction to the heating system to reduce any error.
For example if the clothes are too wet the controller may increase the temperature or drying time. Likewise, if the clothes are nearly dry it may reduce the temperature or stop the process so as not to overheat or burn the clothes, etc.

## Slide 13: Cont..
Advantages of closed-loop control system
Accuracy: They are more accurate than open loop system due to their complex construction. They are equally accurate and are not disturbed in the presence of non-linearities.
Noise reduction ability: Since they are composed of a feedback mechanism, so they clear out the errors between input and output signals, and hence remain unaffected to the external noise sources
To reduce errors by automatically adjusting the systems input.
To improve stability of an unstable system.
To increase or reduce the systems sensitivity.
To enhance robustness against external disturbances to the process.
To produce a reliable and repeatable performance

## Slide 14: Cont..
Disadvantages;
Construction: They are relatively more complex in construction and hence it adds up to the cost making it costlier than open loop system.
Since it consists of feedback loop, it may create oscillatory response of the system
Stability: It is less stable than open loop system but this disadvantage can be striked off since we can make the sensitivity of the system very small so as to make the system as stable as possible
The feedback reduces the overall gain of the system

## Slide 15
The End

## Slide 16: Control System Block Diagrams
Block Diagram Representation of Control Systems
A Block Diagram is a shorthand pictorial representation of the cause-and-effect relationship of a system.
The interior of the rectangle representing the block usually contains a description of or the name of the element, or the symbol for the mathematical operation to be performed on the input to yield the output.
The arrows represent the direction of information or signal flow.

## Slide 17: Cont..
The operations of addition and subtraction have a special representation.
The block becomes a small circle, called a summing point, with the appropriate plus or minus sign associated with the arrows entering the circle.
The output is the algebraic sum of the inputs.
Any number of inputs may enter a summing point.
Some books put a cross in the circle.

## Slide 18: Cont..
Now
If a block diagram has many blocks, not all of which are in cascade, then it is useful to have rules for rearranging the diagram such that you end up with only one block.
For example, we would want to transform the following diagram

## Slide 19: Cont..
Block Diagram Transformations

## Slide 20: Cont..

## Slide 21: Cont..
Rule 6
Consider the following simple feedback loop
If we write equations for the above diagram we get:

## Slide 22: Cont..
Substitute (2) into (1) to get
Substitute (4) into (3) to get

## Slide 23: Cont..
Example 1
Consider the following feedback control system:

## Slide 24: Cont..
First, let’s move H2 behind block G4 so that we can isolate the G3 – G4 – H1 feedback loop. Use Rule 4 of Table 1 to get

## Slide 25: Cont..
Now, we can eliminate the 3 4 1 G -G - H loop by using Rule 6 of Table 1:

## Slide 26: Cont..
Now eliminate inner loop using Rule 6
Therefore, the equivalent diagram is

## Slide 27: Cont..
Finally, we can eliminate the last feedback loop to get:
Using block diagrams, it becomes easy to see where new blocks can be added to an existing system to alter system performance.

## Slide 28: Cont..
Example 2:
Reduce the following multi system into a single block diagram

## Slide 29: Cont..
By moving the summing point of the negative feedback loop containing H2 outside the positive loop containing H1, we obtain:
Eliminate the positive feedback loop, we get:

## Slide 30: Cont..
The elimination of the loop containing H2/G1 gives:
Finally, eliminating the feedback loop gives:

## Slide 31: Home Work
Q1
Reduce the following multi system into a single block diagram

## Slide 32: Cont..
Q2
Simplify the following block diagram into a single block

## Slide 33
The End

## Slide 34: Signal Flow Graphs
For complex control systems, the block diagram reduction technique is cumbersome.
An alternative method for determining the relationship between system variables has been developed by Mason and is based on a signal flow graph.
A signal flow graph is a diagram that consists of nodes that are connected by branches. A node is assigned to each variable of interest in the system, and branches are used to relate the different variables.
The main advantage for using SFG is that a straight forward procedure is available for finding the transfer function in which it is not necessary to move pickoff point around or to redraw the system several times as with block diagram manipulations.

## Slide 35: Cont..
In other words
Signal flow graphs are a pictorial representation of the simultaneous equations describing a system.
Signal flow graphs display the transmission of signals through the system, as does the block diagrams, but it is easier to draw and easier to manipulate than the block diagrams.
Unlike block diagrams, which consist of blocks, signals, summing junctions, and pickoff points, a signal-flow graph consists only of branches, which represent systems, and nodes, which represent signals.

## Slide 36: Cont..
SFG is a diagram that represents a set of simultaneous linear algebraic equations which describe a system. Let us consider an equation, y = ax. It may be represented graphically as;
Terminologies:
Node: A junction denoting a variable or a signal.
Branch: A unidirectional path that relates the dependency of an input and an output.
  Relation between variables is written next to the directional arrow.
Path: A branch or a continuous sequence of branches that can be traversed from one node to another

## Slide 37: Cont..
An input node or source contain only the outgoing branches. i.e., X1
An output node or sink contain only the incoming branches. i.e., X4
A path is a continuous, unidirectional succession of branches along which no node is passed more than ones. i.e., X1 to X2 to X3 to X4, X2 to X3 back to X2, X1 to X2 to X4, are paths.
A forward path is a path from the input node to the output node. i.e., X1 to X2 to X3 to X4, and X1 to X2 to X4, are forward paths.

## Slide 38: Cont..
A feedback path or feedback loop is a path which originates and terminates on the same node. i.e.; X2 to X3 and back to X2 is a feedback path.
A self-loop is a feedback loop consisting of a single branch. i.e.; A33 is a self loop.
The gain of a branch is the transmission function of that branch when the transmission function is a multiplicative operator. i.e., A33
The path gain is the product of branch gains encountered in traversing a path. i.e., X1 to X2 to X3 to X4 is A21A32A43
The loop gain is the product of the branch gains of the loop. i.e., the loop gain of the feedback loop from X2 to X3 and back to X2 is A32A23.

## Slide 39: Cont..
Consider a simple equation below and draw its signal flow graph:
Xi = AijXj
The signal flow graph of the equation is shown below;
Every variable in a signal flow graph is designed by a Node.
Every transmission function in a signal flow graph is designed by a Branch.
Branches are always unidirectional.
The arrow in the branch denotes the direction of the signal flow.
The variables Xi and Xj are represented by a small dot or circle called a Node.
The transmission function Aij is represented by a line with an arrow called a Branch.

## Slide 40: Cont..
1. The Addition Rule:
The value of the variable designated by a node is equal to the sum of all signals entering the node. This can be represented as;
Example: The signal flow graph for the equation of a line in rectangular coordinates, Y = mX + b, is given below. Since b is a constant it may represent a node or a transmission function

## Slide 41: Cont..
2. The Transmission Rule:
The value of the variable designed by a node is transmitted on every branch leaving that node.
Example: The signal flow graph of the simultaneous equations, Y = 3X, and, Z = -4X, is given in the figure below.

## Slide 42: Cont..
3. The Multiplication Rule:
A cascaded or series connection of n-1 branches with transmission functions , can be replaced by a single branch with a new transmission function equal to the product of the old ones. That is
Example: The signal flow graph of the simultaneous equations Y = 10X, Z = -20Y, is given in

## Slide 43: Cont..
Converting Cascaded Block Diagram into a Signal Flow Graph
First thing is to draw the signal nodes for the system.
Next thing is to interconnect the signal nodes with system branches.
The signal nodes for the system are shown in figure (a).
The interconnection of the nodes with branches that represent the subsystem is shown in figure (b).

## Slide 44: Cont..
Converting Parallel System Block Diagram into a Signal Flow Graph:
First thing is to draw the signal nodes for the system.
Next thing is to interconnect the signal nodes with system branches.
The signal nodes for the system are shown in figure (c).
The interconnection of the nodes with branches that represent the subsystem is shown in figure (d).

## Slide 45: Cont..
Converting Feedback System Block Diagram into a Signal Flow Graph:
First thing is to draw the signal nodes for the system.
Next thing is to interconnect the signal nodes with system branches.
The signal nodes for the system are shown in figure (e).
The interconnection of the nodes with branches that represent the subsystem is shown in figure (f).

## Slide 46: Cont..
Example 1:
Convert the block diagram into a signal flow graph

## Slide 47: Cont..
If desired, simplify the signal-flow graph to the one shown in Figure (c) by eliminating signals that have a single flow in and a single flow out, such as V2(s), V6(s), V7(s), and V8(s).

## Slide 48: Cont..
Example 2:
Consider the signal flow graph below and identify the following
Input node.
Output node.
Forward paths.
Feedback paths.
Self loop.
Determine the loop gains of the feedback loops.
Determine the path gains of the forward paths.

## Slide 49: Cont..
Soln.

## Slide 50: Mason’s Rule (Mason, 1953)
The block diagram reduction technique requires successive application of fundamental relationships in order to arrive at the system transfer function.
On the other hand, Mason’s rule for reducing a signal-flow graph to a single transfer function requires the application of one formula.
The formula was derived by S. J. Mason when he related the signal-flow graph to the simultaneous equations that can be written from the graph.

## Slide 51: Cont..
Mason’s Rule:
The transfer function, T = C(s)/R(s), of a system represented by a signal-flow graph is;
Where
n = number of forward paths.
Pi = the i th forward-path gain.
∆ = 1 - ∑Pj1 + ∑Pj2 - ∑Pj3 +…..
= 1 - ∑ loop gains + ∑ gain products of two non-touching loops - ∑ gain products of three non-touching loops + . . .
∆i = ∆ - ∑ loop gain terms in ∆ that touch the i th forward path: In other words;
∆i is formed by eliminating from ∆ those loop gains that touch the i th forward path.
Notes: Pjk = j th possible product of k nontouching loop gains.

## Slide 52: Cont..
Two loops, paths, or loop and a path are said to be non-touching if they have no nodes in common.
∆ is called the signal flow graph determinant or characteristic function. Since ∆=0 is the system characteristic equation.

## Slide 53: Cont..
Loop gains
Loop gain – total gain (product of individual gains) around
any path in the signal flow graph
  Beginning and ending at the same node
  Not passing through any node more than once

## Slide 54: Cont..
  Here, there are three loops with the following gains:
Forward path gain – gain along any path from the input to the output
  Not passing through any node more than once
  Here, there are two forward paths with the following gains:

## Slide 55: Cont..
Non‐touching loops – loops that do not have any nodes in common
  Here:
Non‐touching loop gains – the product of loop gains from non‐touching loops, taken two, three, four, or more at a time
  Here, there are only two pairs of non‐touching loops

## Slide 56: Cont..
Alternatively

## Slide 57: Cont..

## Slide 58: Cont..

## Slide 59: Cont..

## Slide 60: Cont..

## Slide 61: Cont..
Example 2

## Slide 62: Cont..

## Slide 63: Home Work
Q1.
Determine the control ratio C/R and the canonical block diagram of the feedback control system

## Slide 64: Cont..
Q2.
Apply Mason’s rule to determine the value of C(s)/R(s)
R(s)
C(s)
G1
G2
G3
G7
G6
G8
G5
G4
G9
-H2
-H1
-H3
-H5
-H4

## Slide 65
The End

## Slide 66: Mathematical Modelling of Control System
In studying control systems one must be able to model dynamic systems in mathematical terms and analyze their dynamic characteristics.
A mathematical model of a dynamic system is defined as a set of equations that represents the dynamics of the system accurately, or at least fairly well. Note that, a mathematical model is not unique to a given system. A system may be represented in many different ways and, therefore, may have many mathematical models, depending on one’s perspective.
The dynamics of many systems, whether they are mechanical, electrical, thermal, economic, biological, and so on, may be described in terms of differential equations. Such differential equations may be obtained by using physical laws governing a particular system
Notes: Differential equations: equation that relates functions and their derivatives
Functions – represent physical quantity while derivatives represent their rates of change

## Slide 67: Cont..
In mathematics, a differential equation is an equation that relates one or more functions and their derivatives. In applications, the functions generally represent physical quantities, the derivatives represent their rates of change, and the differential equation defines a relationship between the two
In control system design the most common mathematical models of the behavior of interest are, in:
    the time domain,
    linear ordinary differential equations with constant coefficients, and in the
    frequency or transform domain, transfer functions obtained from time domain descriptions via Laplace transforms.
The response of dynamic system to an input may be obtained if these differential equations are solved.

## Slide 68: Cont..
For example; Newton’s laws for mechanical systems and Kirchhoff’s laws for electrical systems. We must always keep in mind that deriving reasonable mathematical models is the most important part of the entire analysis of control systems.
Model
A model is a simplified representation or abstraction of reality. Reality is generally too complex to model exactly.
Mathematical Model
A set of mathematical equations (e.g., differential eqs.) that describes the input-output behavior of a system.
It is used in:
        Simulation
        Prediction/Forecasting
        Prognostics/Diagnostics
        Design/Performance Evaluation
        Control System Design

## Slide 69: Cont..
Black Box Model
When only input and output are known.
Internal dynamics are either too complex or unknown.
Input
Output
Easy to Model
Grey Box Model
When input and output and some information about the internal dynamics of the system is known.
u(t)
y(t)
Easier than white box Modelling.
y[u(t), t]

## Slide 70: Cont..
White Box Model
When input and output and internal dynamics of the system is known.
u(t)
y(t)
One should know complete knowledge of the system to derive a white box model.

## Slide 71: Cont..
In control system engineering, one can derive mathematical models for
            Electrical systems
            Mechanical systems
            Electromechanical system
            Electronic circuits
It can be in:
            Time domain/frequency domain
            Laplace transformation
            z- transformation
            State space equation
It can be in:
            Distributed / Lumped
            Continuous / Discrete
            Linear / Nonlinear
            Time-variant / Time-invariant
            Stochastic / Deterministic
Notes: Stochastic – having a random probability distribution
Deterministic - philosophical

## Slide 72: Cont..
Time Domain and Laplace Transformation
In time-domain analysis the response of a dynamic system to an input is expressed as a function of time.
It is possible to compute the time response of a system if the nature of input and the mathematical model of the system are known.
Usually, the input signals to control systems are not known fully ahead of time.
It is therefore difficult to express the actual input signals mathematically by simple equations.
The characteristics of actual input signals are a sudden shock, a sudden change, a constant velocity, and constant acceleration.

## Slide 73: Cont..
The dynamic behavior of a system is therefore judged and compared under application of standard test signals – an impulse, a step, a constant velocity, and constant acceleration.
The other standard signal of great importance is a sinusoidal signal.
Time domain analysis examines the amplitude Vs time characteristic of measuring signal

## Slide 74: Cont..
Frequency Domain Analysis
Frequency domain analysis replaces the measured signal with a group of sinusoidal which when added together, produces a waveform equivalent to the original signal. The relative amplitude, frequencies, and phases of the sinusoidal are examined
In time-domain analysis the response of a dynamic system to an input is expressed as a function of time c(t)
It is possible to compute the time response of a system if the nature of input and the mathematical model of the system are known

## Slide 75: Cont..
The time response of a system can be obtained by solving the differential equation governing the system
Alternatively, the response c(t) can be obtained from the transfer function of the system and the input to the system
For closed loop transfer function,
    Response in s-domain, (Laplace transformation)
    C(s) = R(s)*M(s)
    Response in t-domain, (time domain)
    c(t)= inverse Lap[C(s)]

## Slide 76: Cont..
Time Domain Specification
For specifying the desired performance characteristics of a measurement system
These characteristics of a system of any order may be specified in terms of transient response to a unit step input signal
The response of a second order system for a unit input is,
                Peak overshoot
                Settling time
                Steady state error

## Slide 77: Cont..

## Slide 78: Cont..
Settling time: The time taken for a measuring or control instrument to get within a certain distance of a new equilibrium value without subsequently deviating from it by that amount
Rise time: The time required for a pulse to rise from 10 per cent to 90 per cent of its steady value
The delay time is the time required for the response to reach half the final value the very first time.
The peak time is the time required for the response to reach the first peak of the overshoot.
Steady state error: If the output of a control system at steady state does not exactly match with the input, the system is said to have steady state error

## Slide 79: Cont..
Standard Test Signals
Impulse signal
  The impulse signal imitate the sudden shock characteristic of actual input signal.
  If A=1, the impulse signal is called unit impulse signal.
0
t
δ(t)
A

## Slide 80: Cont..
Step signal
  The step signal imitate the sudden change characteristic of actual input signal.
  If A=1, the step signal is called unit step signal
0
t
u(t)
A

## Slide 81: Cont..
Ramp signal
  The ramp signal imitate the constant velocity characteristic of actual input signal.
  If A=1, the ramp signal is called unit ramp signal
0
t
r(t)

## Slide 82: Cont..
Parabolic signal
  The parabolic signal imitate the constant acceleration characteristic of actual input signal.
  If A=1, the parabolic signal is called unit parabolic signal.
0
t
p(t)

## Slide 83: Cont..
Laplace Transform of Test Signals
Impulse
Step

## Slide 84: Cont..
Ramp
Parabolic

## Slide 85: Cont..
Relationship between standard Test Signals

## Slide 86: Cont..
Laplace Transforms for Various Time-Domain Functions

## Slide 87: Cont..
Time Response of Control Systems
Time response of a dynamic system response to an input expressed as a function of time.
The time response of any system has two components
  Transient response
  Steady-state response
System

## Slide 88: Cont..
When the response of the system is changed from equilibrium, it takes some time to settle down. This is called transient response.
The response of the system after the transient response is called steady state response.

## Slide 89: Cont..
Transient response depend upon the system poles only and not on the type of input.
It is therefore sufficient to analyze the transient response using a step input.
The steady-state response depends on system dynamics and the input quantity.
It is then examined using different test signals by final value theorem.

## Slide 90: Cont..
Basic Elements of Electrical Systems

## Slide 91: Cont..
Notes: Capacitance – the ability of a system to store an electric charge

## Slide 92: Cont..
Notes: Inductance – the property of an electric conductor or circuit that causes an electromotive force to be generated by a change in the current flowing

## Slide 93: Cont..
V-I and I-V relations

## Slide 94: Cont..
Example 1
The two-port network shown in the following figure has vi(t) as the input voltage and vo(t) as the output voltage. Find the transfer function Vo(s)/Vi(s) of the network.
Solution
C
i(t)
vi( t)
vo(t)

## Slide 95: Cont..
Taking Laplace transform of both equations, considering initial conditions to zero.
Re-arrange both equations as:
Substitute I(s) in equation on left

## Slide 96: Cont..
Example 2
Write the state equation models for the RLC – circuit below:
Solution
The state equations of the network are obtained by writing the voltages across the inductors and the currents in the capacitor in terms of the three state variables as there are two inductors and one capacitor. The state equations are:

## Slide 97: Cont..
+

## Slide 98: Cont..
In vector - matrix form

## Slide 99: Home Work
Find the transfer functions of the RLC - circuit below i.e ,

## Slide 100: Cont..
Mechanical System
Consider a simple mechanical system, a spring/mass/damper
It consists of a weight m on a spring with spring constant k, its motion damped by friction with coefficient f

## Slide 101: Cont..
If y(t) is the displacement from the resting position and u(t) is the force applied, it can be shown using Newton’s law that the motion is described by the following linear, ordinary differential equation with constant coefficients:
Note that in the next subsection the trajectory y(t) is determined, in terms of the system parameters, the initial conditions, and the applied input force u(t), using a methodology based on Laplace transform

## Slide 102
The End